## Slide 1
Code Workflow
Radio Meteor Tracker -- how the scripts fit together
A living document -- regenerated by build_workflow_pptx.py as the code evolves.
Two views: (1) the DATA pipeline through the modules, and
(2) the OPERATIONAL workflow you follow: setup -> verify -> observe -> analyze.
Radio Meteor Tracker · Code Workflow
code v1.4 · 2026-07-12 · 1/12

## Slide 2
The data pipeline
RF in -> ping out, through the modules
RF in (antenna)
RTL-SDR IQ samples
Band-power + baseline
Detect ping (thresh/hyst)
Classify (inline)
CSV row + snapshot job
- IQ read continuously at 1.024 Msps; each ~4 ms block -> FFT power in the +-90 kHz channel.
- EventDetector: EMA noise-floor baseline + threshold/hysteresis -> a Ping (with sample indices).
- On a ping: the IQ window is pulled from the ring buffer and classify.py labels it INLINE (cheap, so
- the label is ready for the CSV row). The snapshot is handed to a background SnapshotWorker (v1.3).
- KEY INVARIANT: under load the SNAPSHOT is dropped, never the EVENT -- every ping still reaches the CSV,
- so the counts (the science) never degrade under memory or CPU pressure.
Radio Meteor Tracker · Code Workflow
code v1.4 · 2026-07-12 · 2/12

## Slide 3
Modules: who does what
- config.py -- all tunable params (frozen dataclass) + PROFILES (e.g. 'pi').
  . rtl_sdr_env.py -- registers the bundled librtlsdr DLL dir (imported FIRST).
- Detection core (in meteor_detector.py):
  . BandPowerAnalyzer (FFT band power) -> EventDetector (EMA baseline +
  . threshold/hysteresis) -> CsvSink (writes rows).
- snapshot.py -- IQRingBuffer (preallocated circular) holds recent IQ;
  . extract_window pulls the event; SnapshotWorker writes it off-thread.
- dsp.py -- chunked float32 spectrogram + band_stats. Shared by classify and the
  . renderers; keeps the per-event FFT transient at a few MB, not ~200 MB (v1.4).
- classify.py -- labels each ping from its IQ window (runs INLINE, so it must be cheap).
- reconnect.py -- ReconnectingReader: survives USB/read errors (v1.3).
- capture_engine.py -- runs the SAME core on a background thread, publishing to
  . a queue (injectable source -> headless testable).
- gui_app.py -- Tkinter UI drains that queue. CLI and GUI SHARE the core modules.
Radio Meteor Tracker · Code Workflow
code v1.4 · 2026-07-12 · 3/12

## Slide 4
The operational workflow
The steps you actually follow
1. Setup
2. Verify
3. Choose frequency
4. Observe
5. Analyze
- 1. Setup: bind WinUSB (Zadig), edit config.py. 2. Verify: check_device.py, spectrograph.py.
- 3. Choose frequency: fm_scan.py / fm_vacancy.py (already set to 104.3 MHz).
- 4. Observe: meteor_detector.py (CLI, long runs) or gui_app.py (GUI).
- 5. Analyze: session_report.py (a session) and diurnal.py (many days).
Radio Meteor Tracker · Code Workflow
code v1.4 · 2026-07-12 · 4/12

## Slide 5
Stages 1-2: Setup & Verify
- Setup (once):
  . Bind WinUSB to the dongle via tools/rtl-sdr/zadig.exe (Interface 0).
  . Edit config.py (frequency, gain, thresholds, snapshot options).
- Verify & explore:
  . check_device.py -- opens the dongle, captures IQ, prints tuner/stats.
  . fm_scan.py -- strongest carriers (reception sanity check).
  . fm_vacancy.py -- ranks channels -> find a VACANT one for scatter.
  . spectrograph.py -- one-shot image; live_spectrograph.py -- live waterfall.
  . monitor.py N -- timed headless capture -> power + waterfall PNGs.
Radio Meteor Tracker · Code Workflow
code v1.4 · 2026-07-12 · 5/12

## Slide 6
Stage 3: Observe -- CLI vs GUI (same engine)
- meteor_detector.py (CLI):
  . Best for LONG / unattended runs -- bounded memory, logs to a file.
  . Prints each ping; writes meteor_events.csv + snapshots/.
- gui_app.py (GUI):
  . Best for WATCHING -- Live tab (waterfall + side gallery) and Gallery tab
  . (big image viewer). Live freq/gain/threshold, ping counter, Report button.
  . Not for overnight (thumbnail/list memory grows).
- Both run the identical BandPowerAnalyzer / EventDetector / snapshot / classify
  . code -- the GUI just wraps it in capture_engine.py on a thread.
Radio Meteor Tracker · Code Workflow
code v1.4 · 2026-07-12 · 6/12

## Slide 7
Stage 4: Analyze (science tools)
- session_report.py -- one session: pings-per-hour stacked by class + summary
  . (meteors/hr, span, per-class counts). Also reachable from the GUI 'Report' button.
- diurnal.py -- MANY days: folds meteor-only counts onto local hour-of-day,
  . exposure-normalized with Poisson error bars (the diurnal-curve first project).
- Inputs: meteor_events.csv (+ the snapshots/ images for visual triage).
- Filter matters: analyze meteor-CLASS events; aircraft/sporadic-E contaminate rates.
- Reference reading + the science rationale: references/ and Science_and_Publishability.pptx.
Radio Meteor Tracker · Code Workflow
code v1.4 · 2026-07-12 · 7/12

## Slide 8
Profiles: one codebase, two machines (v1.4)
- Memory is dominated by SNAPSHOTS, not detection. At 1.024 Msps one second of
  . IQ is 8.2 MB, and a queued snapshot job holds a whole event window (4-25 MB).
- config.py PROFILES['pi'] -- select with METEOR_PROFILE=pi or --profile pi:
  . snapshot_mode='npz' -- the Pi does NOT render. matplotlib is never imported
    . (~90 MB of RSS) and no multi-second render runs on a slow ARM core.
  . snapshot_queue_max_BYTES -- bounding the queue by job COUNT bounds nothing.
  . snapshot_max_window_s / _max_rows -- cap any one job; shrink the ring.
  . snapshot_skip_aircraft -- near SeaTac these dominate the burst.
- Measured (tools/mem_soak.py, synthetic event flood):
  . pi profile ~104 MB peak RSS | desktop defaults ~450-490 MB
- The Pi captures; your PC renders: render_snapshots.py turns .npz -> PNG.
Radio Meteor Tracker · Code Workflow
code v1.4 · 2026-07-12 · 8/12

## Slide 9
Data artifacts & how they connect
- meteor_events.csv -- one row per ping: start_utc, duration_s, peak_snr_db,
  . peak_power_db, classification. (Old 4-col files auto-rotate to .old.)
- snapshots/ping_<UTC>_<class>.png -- one zoomed spectrogram per ping (snapshot_mode
  . ='png', the Windows default); the class is in the filename.
- snapshots/ping_<UTC>_<class>.npz -- the Pi's compact float16 spectrogram (~1-2 MB);
  . render to PNG on a PC with render_snapshots.py. Same image either way.
- Diagnostics: monitor_power.png / monitor_waterfall.png, spectrograph.png.
- Analysis outputs: session_report.png, diurnal.png.
- Everything downstream keys off meteor_events.csv + snapshots/ -- stable contract.
Radio Meteor Tracker · Code Workflow
code v1.4 · 2026-07-12 · 9/12

## Slide 10
Command cheat-sheet
Command | Purpose | Output
python check_device.py | Confirm the dongle works | console
python fm_vacancy.py | Find a vacant FM channel | console
python live_spectrograph.py 104.3 | Watch the channel live | GUI window
python monitor.py 600 | Timed diagnostic capture | monitor_*.png
python meteor_detector.py | Run detector (CLI, long runs) | CSV + snapshots/
python meteor_detector.py --profile pi | Same, 1 GB Raspberry Pi budget | CSV + .npz snapshots
python gui_app.py | GUI detector (Live/Gallery) | CSV + snapshots/ + view
python render_snapshots.py --dir D:\pi_snaps | Render the Pi's .npz -> PNG (on the PC) | snapshots/*.png
python tools/mem_soak.py --profile pi | Flood the pipeline, report peak RSS | console (PASS/FAIL)
python session_report.py | Per-session pings/hour | session_report.png
python diurnal.py | Rate vs local hour (multi-day) | diurnal.png
Radio Meteor Tracker · Code Workflow
code v1.4 · 2026-07-12 · 10/12

## Slide 11
How this evolves (living document)
- This deck is generated by build_workflow_pptx.py -- edit it and re-run to update.
- Landed (no change to the pipeline SHAPE -- each slots into the existing path):
  . v1.3 auto-reconnect -> wraps the read loop (reconnect.py).
  . v1.3 async snapshots -> SnapshotWorker between 'detect' and 'save'.
  . v1.4 low-memory profile -> dsp.py under classify/render; npz mode; byte-
    . bounded queue; render_snapshots.py added AFTER the pipeline, on the PC.
- Next:
  . Real-hardware validation on an actual Pi (all v1.3/v1.4 work is so far
    . verified headlessly on Windows against synthetic sources).
  . Trained (vs heuristic) classifier -- drops into classify.py, same contract.
  . New analysis tools -> just read meteor_events.csv (stable contract) + snapshots/.
- Keep the module diagram and cheat-sheet in sync as scripts are added/renamed.
Radio Meteor Tracker · Code Workflow
code v1.4 · 2026-07-12 · 11/12

## Slide 12
Summary
- Data path: RF -> IQ -> band-power/baseline -> ping -> classify+snapshot -> CSV/snapshots -> analysis.
- Human path: setup -> verify -> choose frequency -> observe (CLI or GUI) -> analyze.
- CLI and GUI share one detection core; the GUI adds a threaded engine + tabs.
- One codebase, two machines: config.py PROFILES['pi'] fits the same core in 1 GB.
- Stable contract: meteor_events.csv + snapshots/ feed all analysis. Under load the
  . snapshot is dropped, never the event -- the counts always survive.
- Living doc -- regenerate with build_workflow_pptx.py after each iteration.
Radio Meteor Tracker · Code Workflow
code v1.4 · 2026-07-12 · 12/12