## Slide 1
Radio Meteor Tracker
RTL-SDR FM forward-scatter meteor detection | Seattle, WA
Design, status, and roadmap
Release v1.2 - GUI, Classification & Reporting
Detect meteors by the radio echoes their ionized trails reflect from a
distant FM transmitter that is normally below the horizon.
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 1/17

## Slide 2
What is radio meteor forward-scatter?
- A meteor entering the atmosphere (~80-120 km) leaves a brief trail of
  . ionized gas that reflects VHF radio like a mirror.
- Point the receiver at a powerful transmitter far beyond the horizon.
  . Normally you hear nothing (the signal passes overhead).
  . When a trail forms in the common volume, it reflects the signal down
  . to you as a brief 'ping' (a few ms to ~1 s).
- Works day and night, in any weather - a key advantage over visual.
- Count / time-stamp pings to measure meteor activity and shower peaks.
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 2/17

## Slide 3
Choosing the frequency: 104.3 MHz
- Europe has dedicated beacons (GRAVES 143.05 MHz); North America does not.
- -> Use FM broadcast forward-scatter: a channel VACANT locally but carrying
  . a high-power station a few hundred km away.
- Measured the Seattle FM band with the dongle (fm_vacancy.py):
  . 104.3 MHz sits ~12 dB below the noise floor - locally empty.
- Distant co-channel stations on 104.3 (beyond the horizon):
  . KAWO, Boise ID - 52 kW - ~650 km (ideal geometry)
  . KSOP-FM, Salt Lake City UT - 25 kW - ~1100 km (bonus reflector)
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 3/17

## Slide 4
Inputs: Hardware
- RTL-SDR dongle:
  . RTL2832U demodulator + Rafael Micro R820T tuner (USB 0BDA:2838)
  . Delivers raw IQ samples over USB; tunable ~24-1766 MHz
- Antenna:
  . Small whip (used for bring-up). Weak-signal work wants better:
  . horizontal dipole or 3-el Yagi aimed ~SE toward Boise
- Host PC: Windows 11, USB 2.0+
- Driver: WinUSB bound to dongle Interface 0 via Zadig
  . (Interface 1 stays unbound - normal; RTL-SDR uses Interface 0 only)
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 4/17

## Slide 5
Inputs: Software stack
- Python 3.14 (64-bit)
- pyrtlsdr 0.4.0 -> librtlsdr (rtl-sdr-blog v1.3.6 DLLs, bundled)
  . Patched to bind a few optional functions as no-ops (DLL lacks them)
- numpy - FFT / band-power / detection math
- matplotlib - spectrogram & waterfall rendering (Agg for files, TkAgg live)
- python-pptx - this deck
- rtl_sdr_env.py registers the bundled DLL folder so no PATH edits are needed.
- Config-driven: all parameters live in config.py (frozen dataclass).
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 5/17

## Slide 6
How the detector works (pipeline)
- 1. Tune 250 kHz below 104.3 -> whole 180 kHz channel sits at +250 kHz,
  . clear of the RTL-SDR DC spike.
- 2. Read IQ continuously at 1.024 Msps; FFT each ~4 ms block.
- 3. Channel power = sum of FFT power in the +-90 kHz detection band.
- 4. Baseline = slow EMA of channel power while quiet (the noise floor).
- 5. Ping = power rises >= threshold above baseline; ends via hysteresis.
  . Keep only min_ping_ms .. max_ping_ms duration events.
- 6. Log to CSV; (v1.1) save a high-resolution snapshot of the moment.
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 6/17

## Slide 7
Key assumptions
- 104.3 stays locally vacant (no new Seattle station appears on-channel).
- A distant 104.3 carrier (Boise/SLC) is present and stable to reflect.
- Meteor pings are brief (tens of ms to ~1 s) and localized to the channel.
- Events > 2 s are NOT meteors (aircraft scatter, tropo, sporadic-E) -> rejected.
- Fixed gain gives a stable baseline; AGC does not (see next slide).
- The host keeps up with 1.024 Msps USB streaming without dropping samples.
- Single process owns the dongle at a time.
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 7/17

## Slide 8
Bring-up lesson: fixed gain, not AGC
- First 10-min run used gain='auto'. The AGC hunted:
  . startup ramp, mid-run band-wide dips, erratic tail.
  . 6 'pings' logged - all AGC artifacts, 0 real.
- Fixes folded into the baseline config:
  . FIXED gain 40.2 dB (stable baseline ~0.7 dB sigma)
  . warmup_skip_s = 20 s (ignore settling)
  . max_ping_ms = 2000 (reject aircraft/tropo)
  . threshold 6 -> 4 dB (still ~6 sigma)
- Re-run baseline is flat (see plot) -> trustworthy detection.
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 8/17

## Slide 9
Proof: real RF off the antenna
- Spectrograph of live FM capture confirms the full chain works:
  . antenna -> dongle -> WinUSB -> Python -> image.
- Bright vertical bands = local FM stations at exact channel freqs.
- Flickering texture = live audio modulation (proves it is real signal,
  . not an artifact).
- The vacancy scan then found 104.3 clear for meteor scatter.
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 9/17

## Slide 10
v1.1: Trigger snapshots
- Problem: a ping COUNT cannot tell meteor from aircraft or interference.
- Solution: keep a rolling IQ buffer; on each ping, render a zoomed
  . spectrogram (pre-roll + event + post-roll) marked with the channel.
- New: snapshot.py (IQRingBuffer + save_snapshot).
- Changed: Ping carries sample indices; detector records them; main() saves
  . a PNG per ping under snapshots/. Snapshot errors never stop capture.
- Reading a snapshot:
  . Meteor -> brief streak LOCALIZED at 104.3 (maybe a Doppler tail)
  . Aircraft -> a carrier line SWEEPING in frequency over seconds
  . Interference -> broadband smear across the whole window
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 10/17

## Slide 11
v1.2: GUI, classification & reporting
- Threaded capture engine (capture_engine.py) keeps the UI responsive.
- Tkinter GUI (gui_app.py): live waterfall, Start/Stop, live freq/gain/
  . threshold, ping counter, per-class tally, and a snapshot GALLERY
  . with class-colored thumbnails (click to enlarge).
- Auto classification (classify.py) of every ping:
  . meteor / aircraft / interference, from spectral concentration,
  . frequency drift, and duration. Written to CSV, filename & GUI.
- Session report (session_report.py): pings-per-hour stacked by class,
  . plus a text summary (example at right).
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 11/17

## Slide 12
v1.3: Tabbed UI + surviving a long run
- GUI split into a ttk.Notebook: Live tab (waterfall + side gallery) and
  . Gallery tab (big image viewer, Prev/Next, full event list).
- Problem: an overnight run could not be trusted to finish.
- Auto-reconnect (reconnect.py -> ReconnectingReader): a USB/read error no longer
  . ends the run -- close -> exponential backoff -> reopen -> resume.
- Async snapshots (snapshot.py -> SnapshotWorker): matplotlib rendering moved to a
  . background thread, so it never stalls the capture read and drops USB samples.
  . If the worker falls behind, extra RENDERS are dropped -- events still logged.
- Shared by CLI, GUI and the Pi service. CLI prints a 5-minute heartbeat.
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 12/17

## Slide 13
v1.4: Fitting a 1 GB Raspberry Pi (this release)
- The insight: memory is dominated by SNAPSHOTS, not detection.
  . One second of IQ at 1.024 Msps = 8.2 MB. A queued snapshot job holds a whole
  . event window: ~4 MB (brief meteor) to ~25 MB (2 s event).
  . v1.3's 32-JOB queue bound was really a ~790 MB bound -> OOM on a Pi during an
    . aircraft burst, which is exactly when the queue fills.
- Fixes (all shared by CLI / GUI / Pi):
  . Queue bounded by BYTES. dsp.py: chunked float32 FFT (numpy upcasts to complex128,
    . so the old one-shot FFT spiked ~150-200 MB PER EVENT). Ring buffer is now
    . preallocated + circular (was re-allocating ~33 MB four times a second).
  . snapshot_mode = png | npz | off. On the Pi, matplotlib is never imported (~90 MB)
    . -- events are saved as compact .npz and rendered on a PC (render_snapshots.py).
- Measured: ~104 MB peak RSS on the 'pi' profile vs ~450-490 MB on the defaults.
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 13/17

## Slide 14
Version roadmap
- v1.0 - Baseline detector
  . Band-power + EMA baseline + threshold/hysteresis -> CSV log & count.
  . Hardened: fixed gain, warm-up skip, duration bounds.
- v1.1 - Trigger snapshots
  . Rolling IQ buffer; per-ping high-res spectrogram.
- v1.2 - GUI, classification & reporting
  . Threaded engine; live waterfall + counter + snapshot gallery.
  . Heuristic meteor/aircraft/interference classifier; session reports.
- v1.3 - Tabbed UI + long-run robustness
  . Live/Gallery tabs; auto-reconnect; async snapshots off the capture thread.
- v1.4 - Low-memory profile (CURRENT)
  . Fits the 1 GB Pi 3B+: byte-bounded queue, chunked FFT, circular ring,
  . npz snapshot mode + PC-side rendering. config.py PROFILES['pi'].
- Next
  . Real-hardware validation on a Pi; trained classifier; dark theme; .exe packaging.
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 14/17

## Slide 15
An observing session: a meteor shower night
- Example: Perseids peak, night of Aug 12-13 (also Delta Aquariids late Jul).
- Before: python fm_vacancy.py to confirm 104.3 still clear; check gain fixed.
- Run: python meteor_detector.py continuously, e.g. 22:00 -> 06:00 local.
  . Snapshots ON; CSV logging the whole night.
- Expect: ping rate RISES after local midnight toward dawn (Earth's leading
  . side faces the meteor stream), and higher near the peak date.
- Watch out: summer sporadic-E can mimic activity - real pings are brief;
  . E-skip openings last minutes and show in snapshots as sustained signal.
- After: review snapshots, classify, plot pings-per-hour vs time & vs sporadic rate.
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 15/17

## Slide 16
Next steps
- Antenna upgrade (biggest sensitivity gain): dipole/Yagi aimed SE to Boise.
- Real-hardware validation of v1.3/v1.4 -- all of it is so far verified HEADLESSLY
  . on Windows against synthetic sources; the Pi run is still pending.
- Frequency calibration: rtl_test -p to set freq_correction_ppm.
- Longer unattended runs (overnight) to gather real event statistics, then
  . tune classifier thresholds against confirmed events. Target: Perseids Aug 12-13.
- Later: trained classifier; dark theme + MHz axis polish; package as an .exe.
- Optional: second reference channel (e.g., 104.5 Spokane) for cross-checking.
- Optional: contribute counts to citizen-science meteor networks.
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 16/17

## Slide 17
Caveats & limitations
- Small whip antenna limits sensitivity -> expect low ping rates for now.
- Summer sporadic-E (Jun-Aug) can cause false pings; distinguish by duration.
- RTL-SDR frequency drift until warmed up / ppm-calibrated.
- Only one process may hold the dongle at a time.
- pyrtlsdr patch lives in site-packages; a reinstall reverts it.
- Classification (v1.2+) is HEURISTIC, not trained -- treat labels as triage, and
  . expect to tune the thresholds in config.py against confirmed events.
- Under heavy load a SNAPSHOT may be dropped (v1.3/v1.4 governors) -- the EVENT is
  . always still classified and logged, so the counts never suffer.
Radio Meteor Tracker · Code & Versions
code v1.4 · 2026-07-12 · 17/17