## Slide 1
DIY Antenna Options
Improving reception for 104.3 MHz FM meteor forward-scatter | Seattle
Goal: hear a distant FM carrier (Boise, ~650 km SE) reflected off meteor
trails. That is a WEAK-signal task -- antenna and location matter a lot.
Bottom line up front: getting OUTSIDE and away from house noise is usually
a bigger win than which antenna you build.
Radio Meteor Tracker · DIY Antenna Options
code v1.5 · 2026-07-13 · 1/10

## Slide 2
The RF you're working with
- Frequency 104.3 MHz -> wavelength (lambda) ~ 2.88 m. Key sizes:
  . quarter-wave ~ 72 cm; half-wave ~ 144 cm (wire ~5% shorter).
- What 'a better antenna' buys you:
  . GAIN on the weak distant path (more pings, fainter pings detected),
  . DIRECTIVITY: aim at Boise (~SE) and reject strong LOCAL Seattle FM,
  . LOWER NOISE: away from house electronics = lower noise floor.
- Polarization: US FM is usually circular/mixed, so H or V both work; prefer
  . HORIZONTAL to cut man-made (often vertical) noise.
- Geometry: meteor echoes arrive from LOW elevation toward the transmitter,
  . so aim ~SE, near the horizon (not straight up).
Radio Meteor Tracker · DIY Antenna Options
code v1.5 · 2026-07-13 · 2/10

## Slide 3
Your current whip: what to expect -- and is it worth it?
- Worth it? YES, as a baseline / proof -- you already saw it receive local FM.
- For WEAK meteor scatter, a small indoor whip is marginal:
  . expect low counts and only the STRONGER pings; many will be missed.
- Quick wins with what you have (no build):
  . If it is the telescopic dipole kit, set each element to ~68-72 cm (1/4-wave).
  . Stand it VERTICAL as a whip, or better, lay the two elements HORIZONTAL
    . in a line for a 1/2-wave dipole.
  . Move it to a window facing SE (toward Boise); get it as high as you can.
- Use the whip to establish a baseline ping rate, then compare after upgrades.
Radio Meteor Tracker · DIY Antenna Options
code v1.5 · 2026-07-13 · 3/10

## Slide 4
Indoor vs outdoor -- the biggest lever
- This likely matters MORE than antenna type.
- Indoors you fight TWO problems:
  . Building loss: walls/roof/low-E windows/foil insulation = ~10-20 dB down.
  . Indoor noise: chargers, LED drivers, PCs, routers raise the VHF noise floor.
- Outdoors, up, and away from electronics can gain ~10-20 dB of SNR -- often
  . the single biggest improvement you can make.
- Progression to try (each step usually helps):
  . SE-facing window -> attic -> outside on a short mast / eave.
- Keep the antenna a few feet from metal gutters, wiring, and the house wall.
Radio Meteor Tracker · DIY Antenna Options
code v1.5 · 2026-07-13 · 4/10

## Slide 5
DIY antenna options at a glance
All dimensions scale to lambda ~ 2.88 m; cut wire ~5% short of the ideal and check with an online calculator.
Antenna | Gain | Pattern | Build | ~Cost | Best for
Stock whip / telescopic | ~0-2 dBi | Omni-ish | none | $0 | baseline / testing
Half-wave dipole (horiz) | ~2 dBi | Bidirectional | Low | $5-15 | easy first upgrade
Folded dipole | ~2 dBi | Bidirectional | Low-Med | $10 | broadband FM
Halo / turnstile | ~0-2 dBi | Omni (H-pol) | Med | $15 | no aiming needed
Moxon (2-element) | ~5-6 dBi | Directional +F/B | Med | $15-25 | compact beam -> Boise
Yagi (3-element) | ~7-8 dBi | Directional | Med-High | $20-40 | best SNR toward Boise
Radio Meteor Tracker · DIY Antenna Options
code v1.5 · 2026-07-13 · 5/10

## Slide 6
Option A: Half-wave dipole (recommended first build)
- Simplest real upgrade. Two wires/rods, each ~68-69 cm, in a straight line
  . (total ~1.37 m), fed at the center.
- Materials: wire or copper tube, coax (RG-6 is cheap & low-loss), and a
  . common-mode choke/balun at the feedpoint (a few ferrite turns of coax).
- Orientation: HORIZONTAL, wire running NE<->SW so the broadside faces SE
  . (dipole is bidirectional: SE and NW lobes; the NW lobe is just unused).
- Pros: cheap, easy, big step up from a small whip, low noise if outside.
- Cons: no front/back rejection of local FM (a beam does that).
Radio Meteor Tracker · DIY Antenna Options
code v1.5 · 2026-07-13 · 6/10

## Slide 7
Option B: Directional -- Moxon or 3-element Yagi (best SNR)
- Adds gain AND rejects strong local Seattle FM coming from other directions
  . -> cleaner detection of the weak Boise path.
- Moxon (2-el): compact rectangle of wire on spreaders; ~5-6 dBi with good
  . front-to-back; forgiving to build. Great value.
- Yagi (3-el): reflector + driven + director on a ~1 m boom; ~7-8 dBi.
  . Elements ~1.3-1.5 m; use a calculator (e.g. for 104.3 MHz).
- Aim the FRONT toward Boise (~SE, azimuth ~120-130 deg), low elevation.
- Mount horizontally for H-pol; needs a small mast and a way to point it.
- Cons: bigger, must be aimed; overkill until you're outside with low noise.
Radio Meteor Tracker · DIY Antenna Options
code v1.5 · 2026-07-13 · 7/10

## Slide 8
Feedline & noise tips (cheap dB you shouldn't skip)
- Coax: RG-6 (75 ohm TV coax) is cheap and low-loss at FM; RTL-SDR is happy
  . with it. Keep runs as short as practical.
- Add a common-mode CHOKE at the feedpoint (coil the coax through a ferrite):
  . stops the coax shield from acting as an antenna and dragging house noise in.
- Route coax away from power wiring, chargers, Ethernet, and the PC.
- Strong local FM can OVERLOAD the RTL-SDR (desense): a directional antenna
  . aimed at Boise + your fixed gain setting both help; back off gain if needed.
- LNA / bias-tee: helps only if you're COAX-loss-limited, not NOISE-limited.
  . At FM with short coax you're usually noise-limited -> an LNA won't help much.
Radio Meteor Tracker · DIY Antenna Options
code v1.5 · 2026-07-13 · 8/10

## Slide 9
Recommended path (cheap -> serious)
- Step 1 (free): tune the whip/dipole to ~68-72 cm elements, horizontal,
  . at an SE window as high as possible. Baseline the ping rate.
- Step 2 ($5-15): build a horizontal half-wave dipole and put it OUTSIDE,
  . broadside to SE, with a feedpoint choke. Expect the biggest jump here.
- Step 3 ($15-40): Moxon or 3-el Yagi aimed at Boise for real counts and
  . rejection of local FM -- worth it once you're outside and noise-limited.
- Re-baseline after each step (same run length) to measure the improvement.
Radio Meteor Tracker · DIY Antenna Options
code v1.5 · 2026-07-13 · 9/10

## Slide 10
Summary
- The current whip is fine to PROVE the system and baseline, but expect low
  . meteor counts, especially indoors.
- Biggest single win: get the antenna OUTSIDE, up, and away from house noise.
- Best cheap build: a horizontal half-wave dipole (~68 cm legs), broadside SE.
- Best performance: a Moxon or 3-el Yagi aimed SE at Boise, once outdoors.
- Feedline hygiene (RG-6 + feedpoint choke, routed away from noise) is free dB.
- Measure each change with an equal-length run so you know what actually helped.
Radio Meteor Tracker · DIY Antenna Options
code v1.5 · 2026-07-13 · 10/10