## Slide 1
Long-Duration Run Planning
Running the meteor detector unattended for 10-12 hours
Goal: capture a full night (ideally near a shower peak) and review it
in the morning via the session report + snapshot gallery.
Radio Meteor Tracker | 104.3 MHz FM forward-scatter | Seattle, WA
Planning only -- no run executed yet.
Radio Meteor Tracker · Long-Duration Run Planning
code v1.5 · 2026-07-13 · 1/12

## Slide 2
What it looks like operationally
- Run the CLI, NOT the GUI, for long unattended sessions:
  . python meteor_detector.py (prints pings, writes CSV + snapshots)
  . Memory is bounded: preallocated IQ ring + a BYTE-bounded snapshot queue.
  . It will run flat for days; a 5-min heartbeat prints pings/reconnects/RSS.
- The GUI is for WATCHING, not overnight logging:
  . it keeps every thumbnail image + growing lists in memory -> balloons
  . over hundreds/thousands of events.
- Morning workflow:
  . python session_report.py -> pings-per-hour chart + summary
  . browse snapshots/ (classified meteor / aircraft / interference).
Radio Meteor Tracker · Long-Duration Run Planning
code v1.5 · 2026-07-13 · 2/12

## Slide 3
Limitations -- ranked by likelihood to bite
- 1. USB glitch ends the run -- FIXED in v1.3 (auto-reconnect).
- 2. Snapshot rendering blocks capture -- FIXED in v1.3 (async worker).
- 3. Seattle air traffic (SeaTac) -> snapshot / disk flood -- GOVERNED (v1.3/v1.4).
- 4. Windows sleep / USB suspend / Update restart can interrupt.
- 5. Thermal drift -- mostly a NON-issue here (wideband detection).
- 6. Analysis burden: many aircraft events to triage.
- The code-side risks are now handled; what is LEFT is operational (4) and
  . human (6). Details on the following slides.
Radio Meteor Tracker · Long-Duration Run Planning
code v1.5 · 2026-07-13 · 3/12

## Slide 4
Limitation 1: USB glitch ends the run -- FIXED (v1.3)
- Over 12 h there is a real chance of:
  . a USB hiccup, a libusb read error, or Windows power-managing the dongle.
- WAS: if sdr.read_samples() threw, the capture loop exited and the rest of the
  . night was lost -- a single transient failure = no data until morning.
- NOW: reconnect.py (ReconnectingReader) wraps every read.
  . On error: close -> exponential backoff (1 s, capped at 30 s) -> reopen ->
    . re-apply freq/gain -> resume. Default: never give up.
  . An in-progress event is discarded and the IQ ring cleared (sample-index
    . continuity breaks across the gap); the noise-floor baseline is kept.
  . Reconnects are counted and shown in the 5-minute heartbeat.
- Config: reconnect_enabled / _backoff_start_s / _backoff_max_s / _give_up_after.
Radio Meteor Tracker · Long-Duration Run Planning
code v1.5 · 2026-07-13 · 4/12

## Slide 5
Limitation 2: Snapshot rendering blocks capture -- FIXED (v1.3/v1.4)
- WAS: snapshots rendered SYNCHRONOUSLY inside the capture loop. matplotlib
  . savefig takes ~150-300 ms per event -- and while rendering, no samples are
  . read, so the RTL-SDR USB buffer can overflow and DROP samples. During a
  . burst that cascades into continuous dropouts.
- NOW: snapshot.py SnapshotWorker renders on a BACKGROUND thread.
  . The capture thread only extracts the IQ window and classifies it (cheap),
    . then hands the job off -- submit is non-blocking.
  . The queue is bounded by BYTES (v1.4): a job holds a whole event window,
    . 4-25 MB, so a job-COUNT bound bounded nothing.
- Backpressure = the governor: over the cap, the SNAPSHOT is dropped and
  . counted -- the EVENT is still classified and written to the CSV. The counts
  . (the science) never degrade under load.
Radio Meteor Tracker · Long-Duration Run Planning
code v1.5 · 2026-07-13 · 5/12

## Slide 6
Limitation 3: Seattle air traffic -> disk flood
Near SeaTac, 104.3 forward-scatter catches many aircraft reflections; each currently saves a PNG.
Scenario | Events / 12 h | PNGs (~200 KB ea) | If raw IQ on (~12 MB ea)
Quiet | ~50 | ~10 MB | ~0.6 GB
Busy (aircraft / E-skip) | ~1,500 | ~300 MB | ~18 GB
- Keep snapshot_save_raw_iq = False (it already is) -- raw IQ is the disk killer.
- Even PNG-only, a busy night is a few hundred MB and a LOT of images to triage.
- NOW GOVERNED: snapshot_skip_aircraft skips exactly these, and the byte-bounded
- queue drops renders (never events) under burst. On the Pi, .npz is ~1-2 MB/event.
Radio Meteor Tracker · Long-Duration Run Planning
code v1.5 · 2026-07-13 · 6/12

## Slide 7
Limitation 4: Windows will try to interrupt you
- System sleep / hibernation: kills capture -> must be disabled.
- USB selective suspend: can suspend the dongle -> disable it.
- Windows Update auto-restart: can reboot mid-run -> pause updates / active hours.
- Fine to leave on: display sleep, screensaver.
- All handled in the pre-flight checklist (next-next slide).
Radio Meteor Tracker · Long-Duration Run Planning
code v1.5 · 2026-07-13 · 7/12

## Slide 8
Limitations 5 & 6
- 5. Thermal drift -- mostly a NON-issue here:
  . the tuner drifts as it warms, but we detect over the WHOLE +-90 kHz
  . FM channel, so a few kHz of drift is irrelevant.
  . (It would matter for a narrowband CW beacon; it does not for us.)
- 6. Analysis burden:
  . a busy night's snapshots are dominated by aircraft.
  . The auto-classifier + per-class session report exist precisely to
  . make triage manageable -- but review is still real work.
Radio Meteor Tracker · Long-Duration Run Planning
code v1.5 · 2026-07-13 · 8/12

## Slide 9
Pre-flight checklist (for when you do it)
- 1. powercfg /change standby-timeout-ac 0 (no system sleep).
- 2. Disable USB selective suspend (dongle + USB Root Hubs, Power Mgmt tab).
- 3. Pause Windows Update for the run window.
- 4. Confirm free disk (budget ~1 GB to be safe).
- 5. Verify nothing else holds the dongle.
- 6. Launch with a log file: python meteor_detector.py *> run_YYYYMMDD.log
- 7. Ideally time it to a shower (Perseids Aug 12-13); rates rise toward dawn.
- 8. Spot-check after ~15 min that pings / CSV / snapshots are flowing, then leave it.
Radio Meteor Tracker · Long-Duration Run Planning
code v1.5 · 2026-07-13 · 9/12

## Slide 10
Robustness upgrades -- BUILT (v1.3 / v1.4)
- These are what make an overnight run trustworthy. All now in the code:
  . Auto-reconnect: retry on USB/read error (close -> backoff -> reopen ->
    . resume). reconnect.py. [limitation 1]
  . Async snapshots: background worker + bounded queue, so rendering never
    . stalls the reader. snapshot.py SnapshotWorker. [limitation 2]
  . Snapshot governor: skip 'aircraft' events and/or drop renders over a BYTE
    . cap -- bounds disk, CPU and memory; events still logged. [limitation 3]
  . Heartbeat: every 5 min the CLI prints uptime, pings, reconnects, RSS, and
    . snapshots saved/dropped -- health confirmable at a glance.
- Verified HEADLESSLY (synthetic sources). A real-hardware overnight run is
  . still the outstanding validation step.
Radio Meteor Tracker · Long-Duration Run Planning
code v1.5 · 2026-07-13 · 10/12

## Slide 11
When to run: meteor shower calendar
Dates recur each year. Radio works day/night and through clouds -- see priorities below.
Shower | Peak | Activity | Note for your radio setup
Quadrantids | Jan 3-4 | High | Sharp ~6h peak; cloudy Seattle -> radio wins
Lyrids | Apr 22-23 | Modest | Minor
Eta Aquariids | May 5-6 | Moderate | Pre-dawn radiant
June daytime (Arietids) | Jun 7-10 | Strong (radio) | DAYTIME -> radio ONLY; run in daylight
S.Delta Aq. / Capricornids | Jul 28-30 | Modest | Good Perseids rehearsal
Perseids | Aug 12-13 | High | Reliable; summer sporadic-E false pings
Orionids | Oct 21-22 | Modest | Fast meteors
Leonids | Nov 17-18 | Modest | Rare storm years
Geminids | Dec 13-14 | Highest | Best annual; all-weather radio edge
Ursids | Dec 22-23 | Low | Minor
* Prioritize: Geminids (Dec) & Quadrantids (Jan) -- radio beats clouded-out visual;
* Perseids (Aug); and June DAYTIME showers -- the 'only radio can see this' moment.
Radio Meteor Tracker · Long-Duration Run Planning
code v1.5 · 2026-07-13 · 11/12

## Slide 12
Summary & recommendation
- The code-side blockers are GONE: auto-reconnect (a glitch no longer ends the
  . night) and async snapshots (bursts no longer drop samples) are BUILT, plus a
  . governor that bounds disk/CPU/memory. A 10-12 h CLI run is ready to attempt.
- What is left is OPERATIONAL, and it is on you, not the code:
  . Windows power/update pre-flight (sleep OFF, USB selective suspend OFF,
    . Updates paused, ~1 GB free disk).
  . Log to a file, and spot-check at ~15 min that pings/CSV/snapshots flow.
  . Neither v1.3 nor v1.4 has yet run against real hardware overnight -- treat
    . the first night as a shakedown as much as an observation.
- Keep snapshot_save_raw_iq=False; leave the snapshot governor on.
- Best payoff: run it on a shower night (Perseids Aug 12-13) and compare
  . pings-per-hour to the expected rise toward dawn.
Radio Meteor Tracker · Long-Duration Run Planning
code v1.5 · 2026-07-13 · 12/12