## Slide 1
Reflection Geometry & the Science of the Count
Why only certain meteors bounce a distant FM station into your antenna
Forward-scatter: a distant FM station, normally below your horizon, is relayed
to you for an instant by a meteor's ionized trail. Each confirmed relay = 1 count.
The geometry decides WHICH meteors you see, WHERE the echo comes from, and
HOW that shapes your diurnal & shower curves and your antenna aim.
Radio Meteor Tracker · Reflection Geometry
code v1.5 · 2026-07-13 · 1/11

## Slide 2
The three players
- TX -- a distant FM transmitter (KAWO Boise, 104.3 MHz, ~650 km), normally BELOW
  . your radio horizon -> that channel is empty noise most of the time.
- RX -- your antenna/RTL-SDR watching the empty channel.
- The meteor trail -- a line of ionized plasma (free electrons) at ~85-120 km,
  . created as the meteoroid ablates. It can briefly reflect VHF radio.
- When the geometry is right, the trail relays TX -> RX and the channel lights up
  . for a fraction of a second: a 'ping' (candidate count).
Radio Meteor Tracker · Reflection Geometry
code v1.5 · 2026-07-13 · 2/11

## Slide 3
The specular / ellipsoid condition
A trail reflects to you only where it is TANGENT to a TX/RX-focus ellipsoid
TX (Boise, 104.3 MHz)
RX (your antenna)
P = reflection point (~100 km up)
meteor trail (tangent here)
- Ellipsoid = all points P where TX->P->RX path length is constant (TX & RX are its foci).
- At the tangent point the two ray angles are equal (ellipse reflection property) = specular condition.
Radio Meteor Tracker · Reflection Geometry
code v1.5 · 2026-07-13 · 3/11

## Slide 4
Why only certain meteors reflect to YOU
- Two conditions must BOTH hold:
  . PLACE -- the trail crosses ~85-120 km over the common volume, AND
  . ORIENTATION -- it is tangent to the ellipsoid there (perpendicular to the
    . bisector of the TX-P-RX angle).
- A trail pointing the wrong way has no tangent point in your illuminated region.
- -> You detect a SUBSET of meteors, never all of them. Undercounting is inherent.
- A trail points AWAY from its radiant, so the RADIANT position controls which
  . meteors can be specular for your particular TX-RX path.
Radio Meteor Tracker · Reflection Geometry
code v1.5 · 2026-07-13 · 4/11

## Slide 5
Hot spots: where the echoes actually come from
- Because trail orientation is fixed by the radiant, the specular solutions cluster
  . in specific PATCHES off to the SIDES of the TX-RX great-circle path.
- Echoes generally do NOT come from the midpoint straight down the Boise line --
  . they come from those side 'hot spots'.
- Shower (single radiant): usually TWO hot-spot regions.
- Sporadics (all radiants): the response smears into a broad sensitivity pattern.
- The hot spots sit ~100 km up and a few hundred km away -> low elevation (next slide).
Radio Meteor Tracker · Reflection Geometry
code v1.5 · 2026-07-13 · 5/11

## Slide 6
From geometry to antenna aim
- Reflection point: ~100 km altitude, a few hundred km distant.
  . -> the echo arrives at a LOW elevation angle (~5-20 deg), near the horizon.
- Direction: toward the path / transmitter -- roughly SE toward Boise.
- So aim antenna gain SE and LOW, not at the zenith:
  . horizontal dipole broadside SE, or a Yagi/Moxon pointed at Boise.
- Max usable TX-RX range ~2000 km (limited by the ~100 km reflection height and
  . the horizon at both ends). 650 km (Boise) sits comfortably inside that.
Radio Meteor Tracker · Reflection Geometry
code v1.5 · 2026-07-13 · 6/11

## Slide 7
Why this shapes the diurnal curve
- Sporadic meteor rate peaks ~06h local: Earth's APEX (its direction of motion)
  . rides highest before dawn -> more meteors, more with usable geometry.
- What you RECORD = the true meteor diurnal CONVOLVED with your fixed geometry
  . + antenna pattern (which radiants have hot spots for you, and when).
- So your radio curve still shows a clear daily rhythm, but its exact shape is a
  . fingerprint of YOUR station -- keep the setup constant so it stays comparable.
Radio Meteor Tracker · Reflection Geometry
code v1.5 · 2026-07-13 · 7/11

## Slide 8
Why shower profiles have structure
- A shower has ONE radiant that drifts across the sky through the night.
- Specular hot spots exist only for certain radiant positions/elevations, so the
  . observed radio rate rises and falls with the radiant's geometry.
- This can produce DOUBLE peaks or gaps that are NOT in the true meteor flux --
  . artifacts of the forward-scatter geometry, not the shower itself.
- Interpreting activity therefore needs the IMO statistical-reduction method,
  . not just raw counts (see the Science deck / references).
Radio Meteor Tracker · Reflection Geometry
code v1.5 · 2026-07-13 · 8/11

## Slide 9
What you actually see: two echo types
- UNDERDENSE trail (low electron density):
  . wave passes through; electrons scatter independently; brief spike with fast
  . exponential decay (<~1 s). The majority of events.
- OVERDENSE trail (high electron density):
  . reflects like a metal cylinder; longer echo (seconds), can flutter/distort as
  . upper-atmosphere winds move the trail.
- Both are real counts; the DURATION distribution carries meteoroid mass-index info.
Radio Meteor Tracker · Reflection Geometry
code v1.5 · 2026-07-13 · 9/11

## Slide 10
From geometry to a 'count' (honest limits)
- Each favorable meteor -> one candidate ping. But aircraft, sporadic-E, lightning,
  . and interference also make bursts -> you must CLASSIFY (meteor vs the rest).
- What you count = a RELATIVE, geometry-weighted meteor rate from a CONSISTENT
- setup -- not absolute flux.
- One modest station CANNOT give absolute flux, velocity, radiant, or orbit.
- Consistency is everything: same frequency, gain, antenna, threshold -> valid
  . day-to-day and shower-to-shower comparisons.
Radio Meteor Tracker · Reflection Geometry
code v1.5 · 2026-07-13 · 10/11

## Slide 11
Summary
- Reflection needs the trail TANGENT to a TX/RX-focus ellipsoid (specular) -- only
  . certain positions AND orientations qualify, so you sample a subset.
- Echoes come from side 'hot spots' ~100 km up at low elevation -> aim antenna SE, low.
- Apex motion + your geometry + antenna pattern together shape the diurnal & shower curves.
- A 'count' = a classified meteor echo: relative, not absolute.
- Filtering (classifier) + a constant setup are what make the counts scientifically meaningful.
Radio Meteor Tracker · Reflection Geometry
code v1.5 · 2026-07-13 · 11/11