## Slide 1
Science from a Modest Radio Meteor Station
What's measurable, what's meaningful, and what an amateur can publish
Single RTL-SDR forward-scatter station, 104.3 MHz FM, Seattle.
Honest take: you won't get orbits from one station -- but consistent COUNTS,
activity PROFILES, and echo statistics are real, contributable science.
Radio Meteor Tracker · Science & Publishability
code v1.5 · 2026-07-13 · 1/11

## Slide 2
What a single forward-scatter station measures
- Directly observable per meteor 'ping':
  . time of occurrence, echo DURATION, peak amplitude/SNR, and (with care)
  . Doppler/shape from the snapshot -> under- vs over-dense classification.
- Aggregated over time:
  . counts per hour/day; activity vs a shower's timeline; diurnal rhythm.
- NOT obtainable from one modest station:
  . orbits, radiant, absolute velocity, true absolute flux (need multi-station
  . / interferometry / calibrated geometry).
- Caveat (per IMO): raw amateur counts are a POOR proxy for true flux -- they
  . are modulated by setup & radiant geometry. Consistency + reduction help.
Radio Meteor Tracker · Science & Publishability
code v1.5 · 2026-07-13 · 2/11

## Slide 3
Meaningful product #1: counts & shower activity profiles
- Count pings per hour continuously; overlay on a shower's expected timeline.
- You can measure:
  . the RISE / PEAK / FALL of a shower and WHEN your local peak occurs,
  . relative activity night-to-night and shower-vs-sporadic contrast.
- Contribute the monthly counts to RMOB (global aggregation since 1993) and
  . compare with other stations -- this is the bread-and-butter amateur product.
- Highest value: DAYTIME showers (e.g. Arietids, ~Jun 7) that ONLY radio can
  . observe -- a genuine niche where amateur radio data matters.
Radio Meteor Tracker · Science & Publishability
code v1.5 · 2026-07-13 · 3/11

## Slide 4
Meaningful product #2: diurnal variation & sporadic background
- The sporadic meteor rate rises and falls each day (max ~06h local, min ~18h)
  . as Earth's leading 'apex' side sweeps up more meteoroids.
- A week of continuous data reproduces this classic sinusoid -- a satisfying,
  . verifiable first result that confirms known physics with YOUR hardware.
- Also visible: seasonal changes in sporadic background; day-to-day weather of
  . the near-Earth meteoroid environment.
- Great teaching / write-up material even before any shower.
Radio Meteor Tracker · Science & Publishability
code v1.5 · 2026-07-13 · 4/11

## Slide 5
Meaningful product #3: echo-duration statistics
- Separate UNDERDENSE (brief, exponential-decay) from OVERDENSE (longer, can
  . last seconds) echoes -- your snapshots already show the difference.
- The DURATION DISTRIBUTION (cumulative log-log of duration vs count) carries
  . information about the meteoroid MASS INDEX of the heavier population.
- Overdense echo duration also has a diurnal signature (linked to upper-atmos
  . chemistry/ozone) -- see the NASA paper in references/.
- Needs decent counts (-> better antenna) but is a real analysis, not just a tally.
Radio Meteor Tracker · Science & Publishability
code v1.5 · 2026-07-13 · 5/11

## Slide 6
Where amateurs actually publish / contribute
- RMOB (Radio Meteor Observing Bulletin): submit monthly counts; appears in the
  . monthly bulletin -- the standard amateur radio-meteor output.
- eMeteorNews: amateur-friendly journal; publishes radio observation reports and
  . shower analyses (a realistic venue for a written-up result).
- IMO / WGN (Journal of the IMO): more formal analyses; collaborative campaigns.
- BRAMS Radio Meteor Zoo (Zooniverse): citizen-science classification of spectra.
- Realistic bar: solo peer-reviewed papers are rare; RMOB + eMeteorNews +
- campaign contributions + catching an unexpected outburst are achievable.
Radio Meteor Tracker · Science & Publishability
code v1.5 · 2026-07-13 · 6/11

## Slide 7
Honest limits of one modest station
- Cannot determine orbits, radiants, or true velocities (need >=2-3 stations
  . with timing/interferometry, or a real radar).
- Absolute flux is hard: rate depends on your antenna pattern, noise floor,
  . threshold, and the radiant's elevation vs your reflection geometry.
- So compare RELATIVE rates from a CONSISTENT setup; note config in an observing
  . log; and apply the IMO statistical-reduction method for activity work.
- Aircraft & sporadic-E contamination must be filtered (your classifier helps).
Radio Meteor Tracker · Science & Publishability
code v1.5 · 2026-07-13 · 7/11

## Slide 8
More data with each antenna step
Each rung roughly doubles what you can claim. Re-baseline with equal-length runs to prove the gain.
Tier | Change | Effort/$ | Signal gain | Science it unlocks
0 | Do nothing: whip, indoors | none | baseline | Learn the pipeline; SEE major shower peaks as rate bumps
1 | Move outside + tune to dipole | $0-15 | ~10-20 dB SNR | Clean diurnal curve; shower profiles; start RMOB submissions
2 | DIY horizontal dipole, outside | $10 | low-noise, stable | Reliable hourly rates; minor showers; begin echo-duration stats
3 | Directional Moxon/Yagi -> Boise | $20-40 | +gain, reject local FM | Robust counts; mass-index (duration) analyses; DAYTIME showers
4 | Bigger / multi-station / interfer. | high | multiple sites | Approach velocity, trajectories/orbits (collaboration, research-grade)
Radio Meteor Tracker · Science & Publishability
code v1.5 · 2026-07-13 · 8/11

## Slide 9
Recommended reading (in references/)
- Downloaded PDFs (open access):
  . SARA 2015 -- 'Detecting meteor radio echoes using the RTL/SDR dongle'
    . (the closest match to our exact setup).
  . Egal et al. 2019 -- 'Solar cycle variation in meteor rates' (arXiv:1902.09422).
  . NASA NTRS -- diurnal variation of overdense echo duration & ozone.
- Online (see references/README.md for links):
  . IMO Radio Observations + statistical reduction method; RMOB; AMS Radio;
  . BRAMS Radio Meteor Zoo (Calders et al. 2016); eMeteorNews; rtl-sdr.com.
- Classic book: McKinley (1961), Meteor Science and Engineering.
Radio Meteor Tracker · Science & Publishability
code v1.5 · 2026-07-13 · 9/11

## Slide 10
Suggested first projects (achievable now -> better)
- 1. Diurnal curve: run ~1 week CONTINUOUSLY (24/7), plot rate vs local hour.
  . Reproduces the ~06h-max / ~18h-min sporadic rhythm. Great first result.
- WHY 24/7, NOT JUST NIGHTS: rate = counts / EXPOSURE. Observe only at
  . night and the unobserved daytime hours look observed-but-empty -- their
  . rate collapses and you MANUFACTURE the very curve you are testing for.
  . v1.5's sessions.csv measures real exposure; running 24/7 also gives the
  . daytime coverage the result needs to mean anything.
- THE CONTROL: also plot --class aircraft. Aircraft follow a HUMAN daily
  . rhythm, nothing like the meteor one. If your meteor curve tracks it, the
  . classifier is leaking and you are plotting air traffic.
- 2. Shower profile: capture Perseids (Aug 12-13); hourly counts vs time;
  . find your local peak; submit the counts to RMOB.
- 3. Echo-duration histogram: underdense vs overdense; log-log duration slope.
- 4. Daytime shower (Arietids, ~Jun): radio-only -- a genuine niche contribution.
- Workflow: FREEZE the setup (freq/gain/threshold/antenna) for the whole run and
  . log it; filter aircraft + sporadic-E before analysis. Any change = new baseline.
Radio Meteor Tracker · Science & Publishability
code v1.5 · 2026-07-13 · 10/11

## Slide 11
Summary
- One modest station yields real, contributable science: COUNTS, activity
  . PROFILES, the DIURNAL curve, and echo-DURATION statistics.
- Publish/contribute via RMOB, eMeteorNews, IMO campaigns, and the Radio Meteor Zoo.
- It CANNOT do orbits/velocity/absolute flux alone -- be honest about that.
- Better antenna (outside -> dipole -> Yagi) steadily unlocks more/better analyses.
- Start with the diurnal-curve project; it confirms your chain and known physics.
- Read the 3 PDFs in references/ first; the SARA 2015 one mirrors your setup.
Radio Meteor Tracker · Science & Publishability
code v1.5 · 2026-07-13 · 11/11